## Slide 1: State of Montana Statewide 9-1-1 Plan Project
9-1-1 Advisory Council Meeting
July 10th, 2019

## Slide 2: Introductions
Federal Engineering
  John Murray - Executive Vice President & COO
  Eric Parry, ENP - Program Manager

## Slide 3: Genesis of Project
House Bill 61
  Passed in 2017
Allows for the creation of a Statewide Plan that needs to address:
  Setting of Priorities for the Montana 9-1-1 System
  Establishing Uniform Standards for 9-1-1 Equipment, Hardware, Software
  Formulating Plans for NG9-1-1 Technology Deployment throughout the State

## Slide 4: Overview of Project
Milestone Deliverables | 
Milestone 1: | Completion of Project Plan and Communications Plan
Milestone 2A: | Completion of First Half of Stakeholder Engagement (PSAP surveys, town hall meetings & PSAP visits/interviews)
Milestone 2B: | Completion of Second Half of Stakeholder Engagement (PSAP surveys, town hall meetings & PSAP visits/interviews)
Milestone 3: | PSAP Inventories
Milestone 4: | ESInet Inventory
Milestone 5: | NG9-1-1 Technology Standards and Requirements
Milestone 6: | PSAP Needs Assessments
Milestone 7: | ESInet Design and Implementation Plan

## Slide 5: What We Did
PSAP Inventories & Needs Assessment
  Captured and documented existing inventory and readiness of PSAPs for evolution to NG9-1-1
  Developed summary of survey data and interview results from each PSAP
  Identified technology, hardware, and software upgrades necessary for PSAP to become NG9-1-1 capable
  Developed transition pathway to NG9-1-1 for each PSAP

## Slide 6: What We Did
ESInet Inventory
  Captured and documented status of the existing statewide 9-1-1 network
  Worked with Vision Net & CenturyLink to obtain current network diagrams, maps and current bandwidth availability and utilization
  Captured existing ESInet inventory

## Slide 7: What We Did
NG9-1-1 Technology Standards and Requirements
  Recommended standards to the State for ESInet, network security, GIS data, call delivery, and call processing based on NG9-1-1 national standards
  Developed a preliminary set of NG9-1-1 technology requirements

## Slide 8: What We Did
NG9-1-1/ESInet Design and Implementation Plan
  Developed and validated ESInet requirements
  Developed recommended requirements, designs and implementation plans for a statewide ESInet

## Slide 9: ESInet Options – Option 1
One Vendor: Acquisition and full implementation of statewide ESInet, NGCS, GIS Services and Hosted CPE.
Advantages:
  Time saved during procurement process.
  A single vendor should be easier to manage.
  A single vendor should deploy faster with a streamlined implementation.
  There should be an assurance of interoperability among all components.
  A single vendor to answer all needs and address all issues.

## Slide 10: ESInet Options – Option 1
One Vendor: Acquisition and full implementation of statewide ESInet, NGCS, GIS Services and Hosted CPE.
Disadvantages:
  Selecting a single vendor could be problematic when NG9-1-1 stakeholders are at different stages of deployment, i.e. PSAP CPE NG9-1-1 readiness.
  Pursuing singular/streamlined solutions may result in stranded investments in equipment, system and network components.
  Cost of solution(s) may be high due to a limited number of vendors capable of providing all components and services.

## Slide 11: ESInet Options – Option 1
One Vendor: Acquisition and full implementation of statewide ESInet, NGCS, GIS Services and Hosted CPE.
Risks:
  If a selected vendor uses subcontractors, there may be no/or little input on individual components of solution.
  Service disruption may occur for all NG9-1-1 stakeholders should a primary or sub-contracted vendor change, or the relationship changes due to solvency or other contractual/business-related issues.

## Slide 12: ESInet Options – Option 2
Two Vendors: Separate procurement from one vendor for ESInet and NGCS and another vendor for Hosted CPE.
Advantages:
  Separating the ESInet and NGCS vendor selection from the CPE vendor selection process provides for flexibility in choosing a vendor that is the best fit to deliver each of the services.
  Two vendors are not difficult to manage.

## Slide 13: ESInet Options – Option 2
Two Vendors: Separate procurement from one vendor for ESInet and NGCS and another vendor for Hosted CPE.
Disadvantages:
  Detailed functional requirements must be developed and cross-referenced to reduce risk of gap in service and system functionality.
  Clear service level objections (SLOs) and/or service level agreements (SLAs) supporting the requirements and gap areas.
  Adaptability may be an issue for PSAP sites that have already began the transition to NG9-1-1.

## Slide 14: ESInet Options – Option 2
Two Vendors: Separate procurement from one vendor for ESInet and NGCS and another vendor for Hosted CPE.
Risks:
  Any change of the vendor(s) that provides the ESInet and NGCS may be complex and disruptive to NG9-1-1 stakeholders on both Ingress and Egress side of the service.

## Slide 15: ESInet Options – Option 3
Three Vendors: Separate procurement of CPE, ESInet and NGCS, and GIS services.
Advantages:
  Will allow increased flexibility in choosing the best vendor for each service.
  There will be an advantage to the consumer in negotiating costs and services among multiple vendors.
Disadvantages:
  Interoperability issues may increase when dealing with multiple vendors.
  Managing multiple vendors will be more difficult and require expanded expertise and oversight.

## Slide 16: ESInet Options – Option 3
Three Vendors: Separate procurement of CPE, ESInet and NGCS, and GIS services.
Risks:
  Any change of the vendor(s) that provides the ESInet and NGCS may be complex and disruptive to NG9-1-1 stakeholders on both Ingress and Egress side of the service.

## Slide 17: ESInet Options – Option 4
Four Vendors: Separate procurement of ESInet, NCGS, GIS services, and Hosted CPE.
Advantages:
  The most flexibility for PSAP sites who are at different stages NG9-1-1 deployment.
Disadvantages:
  With multiple systems and expansive components, there will be few vendors able to integrate said systems and components into a single cohesive solution.
Risks:
  Long term management of four independent vendors will be difficult, requiring expanded expertise and oversight.

## Slide 18: ESInet Options – Option 5
Existing Provider and Network: Leverage the existing 9-1-1 Service Provider and network.
Advantages:
  The intimate knowledge of the existing network, equipment and locations will allow an expedited implementation.
  Utilizing local resources allows for scheduling flexibility and not competing with deployment schedules of other 9-1-1 Service Providers.
Disadvantages:
  A sole source acquisition will require detailed requirements to be defined just as a competitive procurement process, which may be resisted by the existing vendor and stakeholders.

## Slide 19: ESInet Options – Option 5
Risks:
  May be limitations in the knowledge-base and experience of existing vendor deployment and support staff.
  The cost and time to bring these resources up to date may impact anticipated expedited deployment.

## Slide 20: ESInet Options – Option 6
Regional Procurement of Variant Solutions: PSAP sites could be divided into distinct regions. This consideration allows for an introduction of procurement variant to all the options listed in relation to CPE vendor selection. This option lends itself to selecting a vendor(s) that offer a Hosted CPE deployment.
This PSAP Regionalization concept should be explored prior to making procurement strategy and deployment decisions.

## Slide 21: ESInet Options – Option 6
Advantages:
  A regional approach should create cost efficiencies.
  Improved scalability.
  Enhanced security.
  Provide for easier maintenance that is administered on a regional level.
  Provide for additional disaster recovery options and capabilities.
  Standardized policies and procedures for call taking that are relevant to the region.

## Slide 22: ESInet Options – Option 6
Disadvantages:
  May be difficult to gain consensus from all the PSAPs within the region due to perceived loss of control.
Risks:
  Loss of a Host site may result in a region’s isolation if not configured, maintained and diligent focus on adherence to policy and procedures.
22

## Slide 23: Next Steps
Montana 9-1-1 Advisory Council
  Review options
  Develop recommendations
  Continue with PSAP NG centric upgrades
  Develop a long-range implementation plan that includes the Tribal PSAPs
  Provide advice & leadership on ESInet procurement

## Slide 24: Next Steps
9-1-1 Advisory Council Planning Sessions
  Federal Engineering engaged to assist Advisory Council in formalizing Statewide 9-1-1 Plan
  Quarterly sessions (September, December 2019 & March 2020)
  Goal: Statewide 9-1-1 Plan approval and adoption March 2020

## Slide 25: Next Steps
PSAP/Stakeholder Outreach
  Socialize Statewide 9-1-1 Plan with the State of Montana PSAP community
  Review High-Level PSAP Needs Assessments with each PSAP
  Conduct through Town Hall meetings

## Slide 26: Introduction to Next Generation 9-1-1

## Slide 27: Do You Have the Same Telephone You Had in 1968?
Notes: The same phone you had 10 years ago? 2 years ago? Not much longer with that for most of us and our upgrade schedule with the wireless carriers
How about

## Slide 28: Do You Play Music the Same Way You Did in 1968?
Notes: The same phone you had 10 years ago? 2 years ago? Not much longer with that for most of us and our upgrade schedule with the wireless carriers
How about

## Slide 29: Do You Have ANY of the Same Technology You Had in 1968?
Notes: The same phone you had 10 years ago? 2 years ago? Not much longer with that for most of us and our upgrade schedule with the wireless carriers
How about

## Slide 30: Do You Think it is Time for Next Generation 9-1-1?
Why or Why not?
DOES THE PUBLIC?
Notes: Resolving Infrastructure Limitations
Equal Access for Hearing Impaired
More Functionality
Increased Data Sharing with PSAPs, and other emergency service providers & responders
Need for National and International Interoperability
Increased disaster response options
Prepare for Unpredictable Future Services
ANY DEVICE, ANY TIME, ANYWHERE. . .

## Slide 31: What is NG9-1-1?
A simple, open architecture that uses a secured, managed IP network and gateways, to manage information sets supporting:
        Voice & Text Messaging
        Data
        Video, and
        Whatever the Future Holds!

## Slide 32: Next Generation 9-1-1
ANY DEVICE, ANY TIME, ANYWHERE!

## Slide 33: WHY IT IS TIME FOR NG9-1-1
Resolving infrastructure limitations
Easing regionalization logistics
Reducing long term costs – Virtual (hosting) of services
More functionality and optional features
Faster info exchange with other PSAPs
Improved caller location = faster call taking and dispatch
Ability to manage spikes in call volume
Notes: Support a wider range of devices coming on the market
Improve the ability of the network to survive and provide service in disasters
Lower costs – shared services & partnerships
Legacy systems have to gateway to the ESInet, and there is a cost to that
However, no specialized service providers (MPC/VPC/SSP) are needed, so operations expense could be lower
Improve the quantity and quality of data available to 9-1-1 and responders
IP/Standards Platform allows for:
Easier integration of disparate systems
  NCIC, LETS, CAD, Radio, Video, Phone, and ??? all on one IP platform
Improved Data connections:
  Potentially anywhere there is a network connection
  Faster call set up times (Mbps versus Kbps) and faster call completion due to higher bandwidth and modern signaling protocols (NG9-1-1 goal is 2 seconds from last keypress to ring at PSAP)
  Lose the delay created by CAMA trunk call set up
Less expensive connections from the carriers
NG9-1-1 will support direct connections by enterprise to the ESInet from the initial deployment. “Secured” connections are possible, but calls can arrive from the Internet. We need to tell people that, but also say that there are firewalls and other border control functions to mitigate attack, and ultimately, it can be turned off if we need to do that.
Improved redundancy everywhere if implemented correctly
  Border Gateway Protocol peering with multiple carriers
Improved reliability through inherent capability of IP networks to automatically reroute around failures. Experience shows that well engineered IP networks allow communications when other kinds of networks fail, and the reliability is achieved at modest cost and complexity
Employees can answer calls anywhere there’s a network
  Call takers that can’t get in during snowstorms
  Call centers can be moved quickly to another location with network connectivity.
  Don’t need carrier circuits to redirect.

## Slide 34: WIIFM? Benefits of NG9-1-1
We can provide better service
Supports a much wider range of devices and services
Improved coping in disaster situations
Telco competition – non-proprietary solutions that are available “off-the-shelf”
We have a bigger say in our own destiny

## Slide 35: Primary Components of NG9-1-1
CPE (9-1-1 Call Taking Equipment)
Network (IP)
Database
GIS (Graphic MSAG & Auto Location)
IT (Security, Upgrades & Maintenance)

## Slide 36: The Importance of GIS
GIS is Core to NG9-1-1
9-1-1 call routing, location validation, and mapping
GIS road centerlines, address points, PSAP boundaries, and NG9-1-1 Core Services will replace the MSAG, ALI and selective routers
GIS data to be compiled from local sources into regional or statewide datasets
Complete, accurate, up-to-date, and standards-based GIS data essential for NG9-1-1

## Slide 37: Secondary Components of NG9-1-1
Funding
Politics
Personnel Issues
Public Education
PSAP Training
Liability
Legislation
Partnering & Sharing Data

## Slide 38: Transition to NG9-1-1
This will be a statewide system – not a State system
NENA and US DOT developed transition plans
Every PSAP has a say
Not going to happen overnight!

## Slide 39: Regional ESInets – Network of Networks
Interconnects PSAPs & facilitates interoperability
Access
Transfers
Enhanced alternate & contingency routing
Remote PSAP capability
Emergency Notification Systems

## Slide 40: How Regional ESInet Will Work With NG9-1-1
Routing determined based on location at time of call setup
  Emergency Call Routing Function (ECRF)
    Either civic or geo location
Routing can be changed when needed
  Policy Routing Function (PRF)
    Routine or contingency
  Border Control Function (BCF)
Location information arrives with call
Additional data available to be forwarded
Notes: Contract for a statewide Emergency Services IP network (ESInet) through DIR
Lead database development efforts
Support core services e.g. rights management
Allocate costs to state program and Districts

## Slide 41: State of Montana Statewide 9-1-1 Plan Project
Federal Engineering
Stands Ready to Assist &
Thanks You for this Opportunity